## Slide 1: LC-QTOF/MS Condition
1. LC Condition
instrument | Agilent 1290 Infinity |  | 
Column | Poroshell 120, EC-C18 4.6 x 50mm, 2.7 µm Temp: 30℃ |  | 
Moblie phase | A: 0.1% Formic acid in DW B: 0.1% Formic acid in ACN |  | 
Gradient | Time(min) | A(%) | B(%)
 | 0 | 95 | 5
 | 3 | 95 | 5
 | 40 | 0 | 100
 | 50 | 0 | 100
 | 51 | 95 | 5
 | 60 | 95 | 5
Injection | 1uL |  | 
Flow rate | 0.3mL/min |  | 
2. MS/MS Condition
instrument | Agilent 6545 Q-TOF
Ion Polarity | Positive, Negative
Gas Temperature | 250℃
Drying Gas | 10L/min
Nebulize | 35psi
Sheath Gas Temp | 350℃
Sheath Gas Flow | 11L/min
Capillary Voltage | 3500V
Fragmentor | 175V
Skimmer | 65V
Oct 1 RF Vpp | 750V

## Slide 2
1. ALE TIC Scan [Positive]
DW Ext
EtOH Ext

## Slide 3
2. Library searching A) Standards( High Score ) – B) ALE DW [Positive]
A
Score | Name | Formula | m/z | Height
99.95 | 4,8,12-Trimethyl tridecanoic acid | C16 H32 O2 | 274.2741 | 467472
99.92 | Vitetrifolin C | C22 H32 O4 | 378.2639 | 545133
B

## Slide 4
2. Library searching A) Standards( High Score ) – B) ALE DW [Positive]
Score | Name | Formula | m/z | Height
99.9 | Mescaline | C11 H17 N O3 | 229.1546 | 512626
99.87 | Massonianoside B | C25 H32 O10 | 493.2069 | 3160890
A
B

## Slide 5
2. Library searching A) Standards( High Score ) – B) ALE EtOH [Positive]
Score | Name | Formula | m/z | Height
99.9 | Karacoline | C22 H35 N O4 | 378.2639 | 272282
99.9 | Shikonofuran A | C18 H20 O5 | 317.1384 | 521349
A
B

## Slide 6
2. Library searching A) Standards( High Score ) – B) ALE EtOH [Positive]
Score | Name | Formula | m/z | Height
99.9 | 6alpha-Methyl-2alpha,6beta-dihydroxymethylbicyclo[3.1.1]heptane-2al pha-O-glucoside | C16 H28 O7 | 350.2174 | 391457
99.89 | Vitetrifolin C | C22 H32 O4 | 378.2639 | 261193
A
B

## Slide 7
DW Ext
EtOH Ext
1. ALE
TIC Scan [Negative]

## Slide 8
2. Library searching A) Standards( High Score ) – B) ALE DW [Negative]
Score | Name | Formula | m/z | Height
99.95 | Methyl di-alpha-L-rhamnoside | C13 H24 O9 | 323.1348 | 588640
99.91 | Antiarolaldehyde | C10 H12 O5 | 211.0611 | 475074
A
B

## Slide 9
2. Library searching A) Standards( High Score ) – B) ALE DW [Negative]
Score | Name | Formula | m/z | Height
99.88 | Pimpinellin | C13 H10 O5 | 291.0511 | 428399
99.88 | Sanleng acid | C18 H34 O5 | 329.2332 | 418008
A
B

## Slide 10
2. Library searching A) Standards( High Score ) – B) ALE EtOH [Negative]
Score | Name | Formula | m/z | Height
99.89 | (-)2D,4D,6D,8D-Tetramethyl undecanoic acid | C15 H30 O2 | 287.2229 | 450017
99.85 | Sanleng acid | C18 H34 O5 | 329.2333 | 405938
A
B

## Slide 11
2. Library searching A) Standards( High Score ) – B) ALE EtOH [Negative]
Score | Name | Formula | m/z | Height
99.82 | Morroniside | C17 H26 O11 | 405.1402 | 307588
99.82 | Agarobiose dimethylacetal | C14 H26 O11 | 369.1402 | 251155
A
B