Electronic Supplementary Information (ESI)

Hydrogenase biomimetics with redox-active ligands: Synthesis, structure and electrocatalytic studies on Fe2(CO)4(2-dppn)(µ-edt) (edt = ethanedithiolate; dppn = 1,8-bis(diphenylphosphino)naphthalene)

### Shishir Ghosh,a,b,c,* Shahed Rana,b Nathan Hollingsworth,c Michael G. Richmond,d Shariff E. Kabirb and Graeme Hogartha,*

Fig. S1. CVs of [Fe2(CO)4(2-dppn)(-edt)] (3) at various scan rates as shown in the legend (in MeCN, 1 mM solution, supporting electrolyte [NBu4][PF6], scan rate 0.1 Vs-1, glassy carbon electrode, potential vs Fc+/Fc).

Fig. S2. Scan rate dependence of the cathodic and anodic peak currents for the reduction of [Fe2(CO)4(2-dppn)(-edt)] (3) in MeCN (1 mM solution, supporting electrolyte [NBu4][PF6], glassy carbon electrode, potential vs Fc+/Fc). Lines show best linear fit of data.

Fig. S3. Scan rate (ν) dependence of the current function (ip/√ν) for the reduction of [Fe2(CO)4(2-dppn)(-edt)] (3) (1 mM solution in MeCN, supporting electrolyte [NBu4][PF6], glassy carbon electrode, potential vs Fc+/Fc).

Fig. S4. CVs of [Fe2(CO)4(2-dppn)(-edt)] (3) in the absence of acid and in the presence of 1-10 equivalents of CF3CO2H (in MeCN, 1 mM solution, supporting electrolyte [NBu4][PF6], scan rate 0.1 Vs-1, glassy carbon electrode, potential vs Fc+/Fc).

Fig. S1. CVs of [Fe2(CO)4(2-dppn)(-edt)] (3) at various scan rates as shown in the legend (in MeCN, 1 mM solution, supporting electrolyte [NBu4][PF6], scan rate 0.1 Vs-1, glassy carbon electrode, potential vs Fc+/Fc).

Fig. S2. Scan rate dependence of the cathodic and anodic peak currents for the reduction of [Fe2(CO)4(2-dppn)(-edt)] (3) in MeCN (1 mM solution, supporting electrolyte [NBu4][PF6], glassy carbon electrode, potential vs Fc+/Fc). Lines show best linear fit of data.

Fig. S3. Scan rate (ν) dependence of the current function (ip/√ν) for the reduction of [Fe2(CO)4(2-dppn)(-edt)] (3) (1 mM solution in MeCN, supporting electrolyte [NBu4][PF6], glassy carbon electrode, potential vs Fc+/Fc).

Fig. S4. CVs of [Fe2(CO)4(2-dppn)(-edt)] (3) in the absence of acid and in the presence of 1-10 equivalents of CF3CO2H (in MeCN, 1 mM solution, supporting electrolyte [NBu4][PF6], scan rate 0.1 Vs-1, glassy carbon electrode, potential vs Fc+/Fc).